## Slide 1
Smart Metal Detection System
ESP32-based IoT Solution with Adafruit IO Integration
Automated sorting system with real-time monitoring and remote control

## Slide 2
Project Overview
Smart Detection:
Automatically detects objects
using IR sensor and identifies metal content with
dedicated metal sensor
IoT Integration:
Real-time data transmission to
Adafruit IO platform for remote monitoring and
control
Automated Sorting:
Relay-controlled
mechanism sorts objects based on metal
detection with manual override capability
Real-time Monitoring:
Tracks object count and
metal detection status with visual and audio
feedback
System Architecture
ESP32 Microcontroller
IR Sensor
Metal Sensor
WiFi + MQTT
Adafruit IO Cloud
Relay Control
LED + Buzzer

## Slide 3
Main Components of the Logic
WiFi & MQTT Setup
Establishes connection to WiFi network and
Adafruit IO
via
MQTT protocol. Subscribes to relay-control feed and
publishes to object-count and metal feeds.
Object Detection
IR sensor
detects objects passing through the system.
Uses state tracking to avoid duplicate counting and
publishes count updates to the cloud.
Metal Detection
Metal sensor
identifies metallic objects. Triggers LED
indicators, buzzer alerts, and controls relay operation
based on detection results.
Relay Control Logic
Supports both
automatic mode
(based on metal
detection) and
manual mode
(remote control via Adafruit
IO commands).

## Slide 4
WiFi and MQTT Setup
WiFi Configuration
The ESP32 connects to the local WiFi network using credentials:
const char*
ssid
= "Moto";
const char*
password
= "123456789";
void
connectToWiFi
() {
WiFi.begin(ssid, password);
while (WiFi.status() != WL_CONNECTED) {
delay(500);
}
}
MQTT Client Setup
Adafruit IO connection parameters:
#define
AIO_SERVER
"io.adafruit.com"
#define
AIO_SERVERPORT
1883
#define
AIO_USERNAME
"username"
#define
AIO_KEY
"key here"
Adafruit_MQTT_Client
mqtt(&client, AIO_SERVER,
AIO_SERVERPORT, AIO_USERNAME, AIO_KEY);
1
Initialize WiFi Client
Create WiFi client object
2
Connect to WiFi Network
Using SSID and password
3
Initialize MQTT Client
With Adafruit IO server details
4
Subscribe to Control Feed
Listen for relay-control commands
5
Publish to Data Feeds
Send object count and metal status

## Slide 5
Object Detection with IR Sensor
How It Works
The IR sensor emits infrared light and detects its reflection.
When an object passes through:
Sensor output changes from
HIGH to LOW
System detects this state change
Object counter increments
Count is published to Adafruit IO
Implementation
The system uses a state flag (
laserState
) to prevent
multiple counts of the same object.
bool objectDetected = digitalRead(IR_SENSOR) == LOW;
if (laserState == HIGH && objectDetected) {
count++;
laserState = LOW;
countFeed.publish((int32_t)count);
} else if (!objectDetected) {
laserState = HIGH;
}
Object Detection Process

## Slide 6
Metal Detection
How It Works
The metal sensor monitors objects passing through the system. When metal is detected, it triggers visual and audio indicators and controls the relay based on the current mode.
Implementation
The metal detection logic checks the sensor pin and takes
appropriate actions:
// Metal detection (only in AUTO mode)
bool metalDetected = digitalRead(METAL_SENSOR_PIN) ==
LOW;
if (!manualRelayMode) {
if (metalDetected) {
// No metal detected actions
digitalWrite(RELAY, HIGH);
} else {
// Metal detected actions
digitalWrite(RELAY, LOW);
}
}
1
Object passes through metal detector sensor
2
System checks if in automatic or manual mode
3
If metal detected: Red LED + Buzzer ON
4
If metal detected: Relay turns OFF (in auto mode)
5
Metal detection status sent to Adafruit IO

## Slide 7
Relay Control Logic
Automatic Mode
Default behavior where relay control is based on metal detection results.
if (!manualRelayMode) {
if (metalDetected) {
// No metal detected
digitalWrite(RELAY,
HIGH
);
} else {
// Metal detected
digitalWrite(RELAY,
LOW
);
}
}
Object Detected
Metal Sensor Check
If No Metal: Relay ON
If Metal: Relay OFF
Manual Mode
Override automatic behavior with direct commands from Adafruit IO.
if (value.equalsIgnoreCase("ON")) {
digitalWrite(RELAY, HIGH);
manualRelayMode = true
;
} else if (value.equalsIgnoreCase("OFF")) {
digitalWrite(RELAY, LOW);
manualRelayMode = true
;
} else if (value.equalsIgnoreCase("AUTO")) {
manualRelayMode = false
;
}
Command from Adafruit IO
"ON": Relay ON + Manual Mode
"OFF": Relay OFF + Manual Mode
"AUTO": Return to Automatic Mode

## Slide 8
Feed Summary (Adafruit IO)
Feed Name
Purpose
Type
Values
factory.object-count
Number of detected objects
Publish
0, 1, 2, 3, ...
factory.metal
Metal detection status
Publish
"0" (no metal), "1" (metal)
factory.relay-control
Manual relay control
Subscribe
"ON", "OFF", "AUTO"
Data Flow Visualization

## Slide 9
Implementation
1
System Initialization
System powers on and establishes connections to WiFi and Adafruit IO MQTT broker.
2
Object Detection
An object passes through the IR sensor beam. The counter increments
and publishes to
factory.object-count
.
3
Metal Detection & Sorting
No metal:
Green LED on, relay ON, "0" published
Metal:
Red LED & buzzer on, relay OFF, "1" published
4
Remote Control
User sends "OFF" to
relay-control
feed. System enters manual mode.
Later, "AUTO" returns to automatic operation.

## Slide 10
Code Highlights and board connections
Setup Function
void setup()
{
// Configure pin modes
pinMode(METAL_SENSOR_PIN, INPUT);
pinMode(IR_SENSOR, INPUT);
pinMode(LED_GREEN, OUTPUT);
pinMode(LED_RED, OUTPUT);
pinMode(BUZZER, OUTPUT);
pinMode(RELAY, OUTPUT);
// Initialize outputs
digitalWrite(LED_GREEN, LOW);
digitalWrite(LED_RED, LOW);
// Connect to network
connectToWiFi();
mqtt.subscribe(&relayControl);
}
Main Loop
void loop()
{
// Ensure MQTT connection
MQTT_connect();
mqtt.processPackets(1000);
// Object detection logic
bool objectDetected = digitalRead(IR_SENSOR) == LOW;
if (laserState == HIGH && objectDetected) {
count++;
laserState = LOW;
countFeed.publish((int32_t)count);
}
// Metal detection logic
bool metalDetected = digitalRead(METAL_SENSOR_PIN) == LOW;
// Process based on detection...
}